## Slide 1
GNSS Positioning Algorithms
Practical Works
November 2024
Paul Thevenon, ENAC
Jan Bolting, SwiftNav

## Slide 2: Positioning Algorithm
RF Front-end
Baseband Signal Processing
Navigation Algorithm
Intermediate Frequency Samples
Code obs
Carrier obs
Doppler obs
Navigation data bits
Position, Velocity, Timing

## Slide 3: Positioning Algorithm
RF Front-end
Baseband Signal Processing
Navigation Algorithm
Intermediate Frequency Samples
Code obs
Carrier obs
Doppler obs
Navigation data bits
Position, Velocity, Timing
RINEX file
RINEX OBS file
RINEX
NAV file
GNSS raw data
code
carrier phase
Doppler
C/N0
….
GNSS Navigation message
Kepler parameters
satellite clock
satellite hardware bias
ionospheric correction
…

## Slide 4: Positioning Algorithm
Navigation Algorithm
Code obs
Carrier obs
Doppler obs
Navigation data bits
Position, Velocity, Timing
Satellite position and clock
time of emission
relativistic effect
sagnac effect (Earth rotation)
Observation corrections
satellite hardware bias
iono
tropo
Weighted Least Squares estimation
Jacobian computation
Observation prediction
RINEX OBS file
RINEX
NAV file

## Slide 5: Positioning Algorithm
PRX
Satellite position and clock
time of emission
relativistic effect
sagnac effect (Earth rotation)
Observation corrections
satellite hardware bias
iono
tropo
Weighted Least Squares estimation
Jacobian computation
Observation prediction
RINEX OBS file
RINEX
NAV file
PRX CSV file
Navigation Algorithm
Code obs
Carrier obs
Doppler obs
Navigation data bits
Position, Velocity, Timing

## Slide 6: Practical works outline
Focus on the use of pandas, a “Flexible and powerful data analysis / manipulation library for Python”
  Widely used in research and industry
  Open source, 43.8K github stars (as of Nov 2024)
Process real data from the IGS (International GNSS Service) data
  TLSE station, hosted in CNES
  24 hours at 30 s interval on 2024-01-01

## Slide 7: Practical works outline
  chapter_0_pandas.md: discover pandas
      select data
      apply functions
      plot
  chapter_1_spp.md: implement a Single Point Positioning solution
      implement observation model
      compute jacobian
      compute WLS
      analyze
  chapter_2_dgnss.md: implement a Differential GNSS solution
      apply differential corrections from a nearby base station
  chapter_3_rtk.md: implement a Real-Time Kinematics solution
      use differentially-corrected code and carrier observations
      Apply WLS over a batch of epochs (instead of a per epoch estimation)

## Slide 8: Practical works outline
  Folder structure
    data/
    instructions/
    src/ <= code here!!
    tests/
  Detailed instructions will guide you through the coding of the various required functions
    After each implementation, unit tests have been written
  Use this powerpoint to put your answers and your results
  The final mark will depend on
    the number of passed tests
    the answers in this powerpoint
    the figures in this powerpoint

## Slide 9: Practical works outline
Positioning accuracy leaderboard🏅
  A leaderboard will be updated with the accuracy of your best solution for each algorithm
Treasure hunt 💰
  We added a playful challenge that you can solve if you reach the goals of all the project.
  The folder “data/treasure_hunt” contains some particular GNSS observations.
    Each group shall choose a couple of files
  Try to process them with your different positioning algorithms to unlock clues!!

## Slide 10: Chapter 0: pandas

## Slide 11: Misc questions
How many observations are there for GPS L1C signals from healthy satellites over 24 hours?
What is the min/max value of the iono delay?
Paste your figure generated by plot_nsat_vs_elevation_mask

## Slide 12: Chapter 1: SPP

## Slide 13: SPP solution
Paste your ENU error figure.
Include your score.
Comment the statistical description of the positioning error.

## Slide 14: SPP residuals (optional)
Paste your estimation residual figure.
Describe the statistical properties of the residuals.
Which factors contribute to large residuals?

## Slide 15: Improved SPP solution (optional)
Paste your ENU error figure for the improved SPP solution.
Include your score.
Comment the statistical description of the positioning error.
Why has it improved?

## Slide 16: SPP - Treasure hunt
Paste your ENU error figure for SPP solution on the longitude file of the treasure hunt

## Slide 17: Chapter 2: DGNSS

## Slide 18: DGNSS solution
Paste your ENU error figure.
Include your score.
Comment the statistical description of the positioning error.
Which errors were reduced by differential corrections?

## Slide 19: DGNSS residuals (optional)
Paste your estimation residual figure.
Compared to SPP, which errors were reduced by differential corrections?
Did any error sources increase?

## Slide 20: DGNSS - Treasure hunt
Paste your ENU error figure for DGNSS solution on the longitude file of the treasure hunt

## Slide 21: Chapter 3: RTK

## Slide 22: Cycle slips
How many cycle slips have been detected by the rover and base receivers?

## Slide 23: Batch problem size
For a clean interval, what is the size of the problem:
  number of epochs in the selected interval,
  total number of observations,
  total number of states (position, clock, ambiguities).

## Slide 24: RTK solution
Paste your ENU error figure.
Include your score.
Comment the statistical description of the positioning error.
What is the strongest assumption to be able to use this positioning algorithm?
Comment on the validity of such assumption for different classes of users: smartphones, automotive, aviation, geodesy

## Slide 25: RTK solution
Paste your ENU error figure.
Include your score.
Comment the statistical description of the positioning error.
What is the strongest assumption to be able to use this positioning algorithm?
Comment on the validity of such assumption for different classes of users: smartphones, automotive, aviation, geodesy

## Slide 26: RTK - Treasure hunt
Paste your ENU error figure for RTK solution on the latitude file of the treasure hunt